## Slide 1
HACK@DAC 2026 — PHASE 2 CALIPTRA RTL AUDIT
RTL Security Analysis & Verification Strategy
Comprehensive Audit of 29 IP Cores: Stage 0 Recon ➔ Phase 1: AI-Orchestrated Dynamic Simulation ➔ Phase 2: Python SAST & AI Validation Pipeline
TEAM LOGICRON
Society for Electronic Transactions and Security (SETS), Chennai, India
Advisor: A. Suganya
Participants: Eswari Devi • Renita .J • Sathish Kumar • Kushana Shyam Sundar
STATUS: Phase 1 Dynamic Simulation (34 Bugs) Complete | Phase 2 Static SAST Pipeline Operational

## Slide 2
TEAM PHOTO
Team LOGICRON — Society for Electronic Transactions and Security (SETS)

## Slide 3
SETS CHENNAI — TEAM LOGICRON | HACK@DAC 2026 CALIPTRA AUDIT
Security Audit Workflow & Phase Separation
STAGE 0: RECONNAISSANCE
IP Discovery & Mapping
• Scope & IP Tree Mapping (29 IPs)
• Register & RDL Specification Audit
• Boundary & Interface Triage
• Threat Modeling & Security Goals
PHASE 1: DYNAMIC ANALYSIS
AI-Orchestrated Simulation
• Claude Code CLI Integration
• Orchestrator AI Batch Scheduling
• Worker AI Instances & Custom Tools
• Runnable PoC Exploits & VCD Traces
PHASE 2: STATIC SAST PIPELINE
Python Engine & AI Validation
• Modular Parallel Static Scanning
• Rule-Based Vulnerability Detection
• Claude AI Root-Cause & FP Reduction
• Exploit Generation & Reproduction

## Slide 4
SETS CHENNAI — TEAM LOGICRON | HACK@DAC 2026 CALIPTRA AUDIT
Stage 0 — Target Subsystem Inventory & Tier Breakdown
Tier | Subsystem Category | Target IP Cores Included | Module Count
Tier 1 | Crypto Cores | AES, SHA-256, SHA-512, SHA-512M, SHA-3, HMAC, HMAC-DRBG, KMAC, ECC, DOE, ML-DSA | 11 IPs
Tier 2 | Storage & Access Control | Key Vault, PCR Vault, Data Vault, Lifecycle Controller | 4 IPs
Tier 3 | Entropy & RNG | CSRNG, Entropy Source, EDN | 3 IPs
Tier 4 | Interfaces & CPU Core | SoC Interface, SPI Host, UART, VeeR EL2 RISC-V Core | 4 IPs
Tier 5 | Bus Fabric & Infrastructure | AXI, AHB-Lite Bus, Caliptra TL-UL, Caliptra Prim, Prim Generic, Shared Libs, Top Integration | 7 IPs

## Slide 5
SETS CHENNAI — TEAM LOGICRON | HACK@DAC 2026 CALIPTRA AUDIT
Phase 1 — Dynamic Analysis: Claude Code & AI Orchestration
1. Claude Code CLI Integration
Utilized Claude Code CLI integrated directly with SystemVerilog simulation tools (Verilator/Iverilog) to automate testbench generation and waveform analysis.
2. Batch-Wise AI Orchestration
A central Orchestrator AI instance manages target IP analysis batch-wise, allocating isolated IP modules to specialized worker agents in parallel.
3. Tool-Assisted Bug Evaluation
Worker AI instances invoke dedicated verification tools to run simulation stimulus, parse trace logs, and evaluate bugs for their assigned IP core.
4. Verified Exploits & Waveforms
Every accepted bug requires a runnable SystemVerilog PoC exploit and a VCD/FST waveform trace proving the vulnerability with 0 false positives.

## Slide 6
SETS CHENNAI — TEAM LOGICRON | HACK@DAC 2026 CALIPTRA AUDIT
Phase 1 — Dynamic Analysis Results & Compute Ledger
34
Confirmed Bugs (0 False Positives)
34
Runnable PoC Exploits + VCD Waveforms
7.88M
Total Compute Tokens (30 Worker Spawns)
29 / 29
IP Cores Tested (100% Coverage)
Top IP Core Name | Tokens Consumed | Execution / Spawns | Dynamic Findings
SHA-3 | 676,655 tokens | 2 Spawns (~5.0h) | 1 Bug (AHB Bus DoS)
Top Integration | 635,160 tokens | 1 Spawn (~8.3h) | 1 Bug (OTP Fuse Gate Bypass)
ML-DSA / Adams Bridge | 423,462 tokens | 1 Spawn (~1.4h) | 1 Bug (Address Decode Collision)
DOE (Deobfuscation Engine) | 381,629 tokens | 1 Spawn (~0.8h) | 1 Bug (Command Replay)
AES Core | 355,032 tokens | 1 Spawn (~6.1h) | 1 Bug (Reseed Latch)

## Slide 7
SETS CHENNAI — TEAM LOGICRON | HACK@DAC 2026 CALIPTRA AUDIT
Dynamic Deep Dive 1 — Key Vault Key Wiping [KV-002]
BUG SPECIFICATION
Bug ID:
KV-002
Target File:
src/keyvault/rtl/kv_top.sv
CVSSv3.1 Score:
8.4 (High Severity)
Impacted IP:
Key Vault (KV)
Exploit Path:
work/exploits/KV-002_exploit.sv
Waveform Trace:
work/waves/KV-002.vcd
Vulnerability Mechanism:
When any two write clients attempt simultaneous transfer (`kv_multi_write_err`), the error handling logic unconditionally zeroizes ALL 24 key slots in the Key Vault — including write-locked and use-locked key entries that had zero involvement in the collision.
Security Consequence:
Complete Key Vault Denial of Service (DoS). An unprivileged write client can intentionally trigger a single collision with a low-privilege slot to instantly wipe critical root keys, HMAC keys, and unlocked secret material across the entire RoT.
Evidence & Verification:
Proven via Verilator PoC exploit testbench (`KV-002_exploit.sv`). VCD trace shows simultaneous writes to Slot 1 & 2 causing `slot_zeroize_bus` to assert across all 24 slots, clearing locked Slot 0 instantly.

## Slide 8
SETS CHENNAI — TEAM LOGICRON | HACK@DAC 2026 CALIPTRA AUDIT
Dynamic Deep Dive 2 — ECC Verification Register Leak [ECC-001]
BUG SPECIFICATION
Bug ID:
ECC-001
Target File:
src/ecc/rtl/ecc_top.sv
CVSSv3.1 Score:
8.1 (High Severity)
Impacted IP:
Elliptic Curve Cryptography
Exploit Path:
work/exploits/ECC-001_exploit.sv
Waveform Trace:
work/waves/ECC-001.vcd
Vulnerability Mechanism:
The `ECC_VERIFY_R` output register is only cleared upon explicit `ZEROIZE` or debug entry, but is NEVER cleared when an invalid input is passed to the ECDSA signature verification engine hardware error path.
Security Consequence:
Signature Verification Spoofing. If a prior valid signature verification succeeded (setting `ECC_VERIFY_R = VALID`), a subsequent invalid/forged signature submission that triggers an input error fails to reset `ECC_VERIFY_R`, leaving stale VALID status active for firmware.
Evidence & Verification:
Confirmed with PoC exploit simulation (`ECC-001_exploit.sv`). Passing a malformed R/S pair causes hardware error flags to set, but `ECC_VERIFY_R` retains `0x1` (VALID) continuously.

## Slide 9
SETS CHENNAI — TEAM LOGICRON | HACK@DAC 2026 CALIPTRA AUDIT
Dynamic Deep Dive 3 — Top Integration OTP Fuse Gate [INTEG-001]
BUG SPECIFICATION
Bug ID:
INTEG-001
Target File:
src/integration/rtl/caliptra_top.sv:1341
CVSSv3.1 Score:
7.9 (High Severity)
Impacted IP:
Top Integration (INTEG)
Exploit Path:
work/exploits/INTEG-001_exploit.sv
Waveform Trace:
work/waves/INTEG-001.vcd
Vulnerability Mechanism:
`caliptra_top.sv` hardcodes `entropy_src`'s OTP fuse permission (`otp_en_entropy_src_fw_over_i`) to constant `MuBi8True`. This collapses the intended two-factor safety gate (OTP Fuse AND SW register) into SW-only control.
Security Consequence:
TRNG Entropy Injection Attack. Malicious firmware alone can force the TRNG entropy source into firmware-override mode in ANY lifecycle state (including Production). Firmware can inject arbitrary 384-bit attacker-chosen entropy feeding CSRNG seeds!
Evidence & Verification:
Differential PoC exploit verified against unmodified `caliptra_top.sv` vs properly-fused logic. The as-built core matches attacker-chosen entropy byte-for-byte in CSRNG.

## Slide 10
PHASE 2: STATIC ANALYSIS PIPELINE
Hardware RTL SAST Validation Methodology
1. Python Analysis Framework
Pass project directory to SAST framework to automatically traverse SystemVerilog source files.
➔
2. Parallel Static Analysis
Divide analysis into 10 independent scanning modules executing concurrently for high performance.
➔
3. Centralized Finding Collection
Collect findings across modules, merge into central database, and normalize info.
➔
4. Internal SAST Rule Scan
Execute Python SAST engine using validated security rules to correlate detection.
PARALLEL SCANNING MODULE CATEGORIES & COVERAGE EFFICIENCY
Modules: Access Control | Secure Boot | OTP/Fuse Security | Debug Interface | Lifecycle State | Register Protection | Memory Protection | Information Disclosure | Cryptographic Misuse | Privilege Escalation
"Multiple independent analysis modules improve coverage while reducing overall analysis time."

## Slide 11
PHASE 2: AI VALIDATION & REPORTING
AI-Assisted Validation & Reporting Pipeline
1. Claude AI (CLI) Analysis
• Root cause analysis
• RTL code inspection
• Security impact evaluation
• Vulnerability validation
2. Duplicate & FP Filter
Filters findings matching:
• Same RTL logic & root cause
• Same attack path & module
• Invalid reachability/intent
3. Exploit Generation
AI creates reproduction evidence:
• Standalone PoC exploits
• Simulation-based validation
• Reproduction verification
4. Final Security Report
Consolidated Final Deliverables:
• Verified unique findings
• Technical report & summary
• Confirmed exploit evidence
FINAL VERIFICATION & CLASSIFICATION GUARANTEE
• Verified Findings: Successfully validated, reproducible, security impact confirmed with generated PoC exploits. • Not Verified Filtered: Not Reproducible (cannot be reliably triggered) and False Positives (design is secure) are removed.
"Only unique, reproducible, and security-relevant vulnerabilities are included in the final report, ensuring high-confidence SAST validation with minimal false positives."

## Slide 12
REMEDIATION & SUMMARY
Synthesis & Remediation Roadmap
SYNTHESIS OF DYNAMIC & STATIC SECURITY FINDINGS
1. Immediate High-Severity RTL Patching:
Prioritize RTL patches for KV-002 (unconditional key zeroize), ECC-001 (verify output leak), RVCORE-001 (PMP bypass), and INTEG-001 (OTP gate hardcode).
2. Standardize Hardware Reset Domains:
Align lock control registers across Key Vault, PCR Vault, and Data Vault to the cold reset domain (`hard_reset_b`) to eliminate post-warm-reset secret exposure.
3. Automated Regression via Dynamic Exploits:
Utilize the 34 developed standalone PoC exploit testbenches (`work/exploits/`) to verify that proposed RTL patches resolve vulnerabilities without introducing regressions.
4. Unified Security Sign-Off:
Combine Phase 1 Dynamic Simulation PoC exploits and Phase 2 Python SAST & AI Validation proofs into a single consolidated audit sign-off package.